Caledonian Mining Cables

AS/NZS 1802:2003 Reeling & Trailing Cables

Type 275 1.1/1.1KV

� Applications .............................................................................................................

These cables are mainly used as a flexible feeder for shuttle cars and pump. Earth cores designed to reduce instances of wire breaks during reeling while under tension.

� Standards .................................................................................................................

AS/NZS 1802:2003

AS/NZS 1125

AS/NZS 3808

AS/NZS 5000.1

� Construction ............................................................................................................

Semiconductive PCP Filling And Covering Reinforcement

Stranded Tinned Copper Conductor Cradle Separator

Central Extensible Pilot EPR Insulation

Earth Conductor

Heavy Duty PCP Sheath

3證onductors: Flexible stranded tinned annealed copper conductor.

Insulation: EPR.

Cradle Separator: Semiconductive PCP.

Overall Core Screen: Semiconductive PCP filling and covering.

3譏nterstitial Earth Conductor: Semiconductive PCP covered flexible stranded tinned copper conductor.

1證entral Extensible Pilot: EPR covered flexible stranded tinned copper conductor.

Textile Reinforcement: Open-weave braid reinforcement.

Sheath: Heavy duty PCP sheath. Heavy duty CPE/CSP sheath can be oﬀered upon request.

www.caledonian-cables.co.uk  www.addison-cables.com	23

Caledonian Mining Cables

AS/NZS 1802:2003 Reeling & Trailing Cables

�  Dimensions and Weight ..........................................................................................

| Nominal Conductor Area | Strand Size | Insulation Thickness | Earth Conductor | Pilot Conductor | Thickness of Sheath Including SC PCP Layer | Nominal Overall Diameter | Nominal Weight |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Strand Size | Thickness of Covering | Strand Size | Thickness of Covering |  |  |  |
| mm� | No/mm | mm | No/mm | mm | No/mm | mm | mm | mm | kg/100m |
| Type 275 |
| 16 | 126/0.40 | 1.6 | 60/0.30 | 1.0 | 24/0.20 | 0.8 | 3.8 | 30.2 | 145 |
| 25 | 209/0.40 | 1.6 | 100/0.30 | 1.0 | 24/0.20 | 0.8 | 4.0 | 33.9 | 204 |
| 35 | 285/0.40 | 1.6 | 140/0.30 | 1.0 | 24/0.20 | 0.8 | 4.3 | 37.9 | 270 |
| 50 | 380/0.40 | 1.7 | 99/0.40 | 1.0 | 40/0.20 | 0.8 | 4.7 | 41.6 | 333 |

24	www.caledonian-cables.co.uk  www.addison-cables.com