Caledonian Mining Cables

AS/NZS 2802:2000 Reeling & Trailing Cables

Type 409 1.1 to 22KV

� Applications .............................................................................................................

Type 409 series cable is mainly used as a flexible feeder to machinery, more suitable as a trailing cable rather than for reeling. Smaller cables are used for drills and hand held tools and equipment, while larger ones are used for power supply to draglines, shovels and drills.

� Standards .................................................................................................................

AS/NZS 2802:2000

AS/NZS 1125

AS/NZS 3808

AS/NZS 5000.1

� Construction ............................................................................................................

Composite Screen

Stranded Tinned Copper Conductor Conductor Screen

Cradle Separator Central Extensible Pilot EPR Insulation Insulation Screen

Heavy Duty PCP Sheath

3證onductors: Flexible stranded tinned annealed copper conductor.

Conductor Screen: Semiconductive compound (for cables having a voltage rating of 3.3/3.3kV and above).

Insulation: EPR.

Insulation Screen: Semiconductive elastomer.

Composite Screen (earth conductor): Tinned annealed copper braiding interwove with polyester yarn.

Cradle Separator: Semiconductive PCP.

1證entral Extensible Pilot: EPR covered flexible stranded tinned copper conductor.

Sheath: Heavy duty PCP sheath. Heavy duty CPE/CSP sheath can be oﬀered upon request.

www.caledonian-cables.co.uk  www.addison-cables.com	25

Caledonian Mining Cables

AS/NZS 2802:2000 Reeling & Trailing Cables

�  Dimensions and Weight ..........................................................................................

| Nominal Conductor Area | Strand Size | Insulation Thickness | Core Screen | Pilot Conductor | Thickness of Sheath | Nominal Overall Diameter | Nominal Weight |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Strand Size | Area of Screen | Strand Size | Thickness of Covering |  |  |  |
| mm� | No/mm | mm | No/mm | mm� | No/mm | mm | mm | mm | kg/100m |
| Type 409.1 Class2 |
| 6 | 84/0.30 | 1.5 | 7/0.25 | 7.2 | 24/0.20 | 0.8 | 3.8 | 30.0 | 129 |
| 10 | 77/0.40 | 1.5 | 7/0.25 | 8.6 | 24/0.20 | 0.8 | 3.8 | 32.6 | 157 |
| 16 | 126/0.40 | 1.6 | 7/0.25 | 9.6 | 24/0.20 | 0.8 | 4.0 | 35.8 | 197 |
| 25 | 209/0.40 | 1.6 | 7/0.25 | 11.3 | 24/0.20 | 0.8 | 4.3 | 39.7 | 255 |
| 35 | 285/0.40 | 1.6 | 7/0.25 | 12.4 | 24/0.20 | 0.8 | 4.6 | 43.1 | 312 |
| 50 | 380/0.40 | 1.7 | 7/0.25 | 14.1 | 40/0.20 | 0.8 | 5.0 | 47.7 | 386 |
| 70 | 203/0.67 | 1.8 | 7/0.25 | 16.5 | 40/0.20 | 0.8 | 5.4 | 53.9 | 503 |
| 95 | 259/0.67 | 2.0 | 7/0.30 | 21.8 | 40/0.20 | 0.8 | 6.0 | 59.3 | 622 |
| 120 | 336/0.67 | 2.1 | 7/0.30 | 24.7 | 40/0.20 | 0.8 | 6.4 | 65.1 | 760 |
| 150 | 427/0.67 | 2.3 | 7/0.40 | 36.1 | 40/0.20 | 0.8 | 6.9 | 72.1 | 960 |
| 185 | 518/0.67 | 2.5 | 7/0.40 | 40.5 | 40/0.20 | 0.8 | 7.4 | 78.6 | 1160 |
| 240 | 672/0.67 | 2.8 | 7/0.50 | 57.7 | 40/0.20 | 0.8 | 8.2 | 88.6 | 1490 |
| 300 | 854/0.67 | 3.0 | 7/0.50 | 63.2 | 40/0.20 | 0.8 | 8.8 | 96.3 | 1800 |
| Type 409.3 Class2 |
| 16 | 126/0.40 | 3.0 | 7/0.25 | 13.1 | 24/0.20 | 0.8 | 5.3 | 46.2 | 301 |
| 25 | 209/0.40 | 3.0 | 7/0.25 | 14.8 | 24/0.20 | 0.8 | 5.6 | 50.1 | 371 |
| 35 | 285/0.40 | 3.0 | 7/0.25 | 15.8 | 24/0.20 | 0.8 | 5.9 | 53.5 | 430 |
| 50 | 380/0.40 | 3.0 | 7/0.25 | 17.2 | 40/0.20 | 0.8 | 6.3 | 57.6 | 511 |
| 70 | 203/0.67 | 3.0 | 7/0.25 | 18.6 | 40/0.20 | 0.8 | 6.6 | 62.5 | 624 |
| 95 | 259/0.67 | 3.0 | 7/0.25 | 20.3 | 40/0.20 | 0.8 | 7.1 | 66.2 | 724 |
| 120 | 336/0.67 | 3.0 | 7/0.30 | 27.2 | 40/0.20 | 0.8 | 7.4 | 72.0 | 880 |
| 150 | 427/0.67 | 3.0 | 7/0.40 | 39.6 | 40/0.20 | 0.8 | 7.8 | 78.0 | 1079 |
| 185 | 518/0.67 | 3.0 | 7/0.40 | 42.2 | 40/0.20 | 0.8 | 8.2 | 83.4 | 1251 |
| 240 | 672/0.67 | 3.0 | 7/0.40 | 46.6 | 40/0.20 | 0.8 | 8.8 | 90.3 | 1502 |
| 300 | 854/0.67 | 3.0 | 7/0.50 | 63.2 | 40/0.20 | 0.8 | 9.4 | 98.4 | 1840 |
| Type 409.6 Class2 |
| 16 | 126/0.40 | 5.0 | 7/0.25 | 17.2 | 24/0.20 | 0.8 | 6.4 | 57.3 | 440 |
| 25 | 209/0.40 | 5.0 | 7/0.25 | 18.6 | 24/0.20 | 0.8 | 6.7 | 61.2 | 516 |

26	www.caledonian-cables.co.uk  www.addison-cables.com

Caledonian Mining Cables

AS/NZS 2802:2000 Reeling & Trailing Cables

| Nominal Conductor Area | Strand Size | Insulation Thickness | Core Screen | Pilot Conductor | Thickness of Sheath | Nominal Overall Diameter | Nominal Weight |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Strand Size | Area of Screen | Strand Size | Thickness of Covering |  |  |  |
| mm� | No/mm | mm | No/mm | mm� | No/mm | mm | mm | mm | kg/100m |
| 35 | 285/0.40 | 5.0 | 7/0.25 | 18.6 | 24/0.20 | 0.8 | 7.0 | 64.6 | 584 |
| 50 | 380/0.40 | 5.0 | 7/0.25 | 21.3 | 40/0.20 | 0.8 | 7.3 | 68.5 | 669 |
| 70 | 203/0.67 | 5.0 | 7/0.25 | 23.4 | 40/0.20 | 0.8 | 7.7 | 73.7 | 804 |
| 95 | 259/0.67 | 5.0 | 7/0.30 | 29.2 | 40/0.20 | 0.8 | 8.1 | 77.8 | 934 |
| 120 | 336/0.67 | 5.0 | 7/0.30 | 31.7 | 40/0.20 | 0.8 | 8.5 | 83.1 | 1090 |
| 150 | 427/0.67 | 5.0 | 7/0.40 | 45.7 | 40/0.20 | 0.8 | 8.9 | 89.1 | 1310 |
| 185 | 518/0.67 | 5.0 | 7/0.40 | 48.4 | 40/0.20 | 0.8 | 9.3 | 94.5 | 1479 |
| 240 | 672/0.67 | 5.0 | 7/0.40 | 52.8 | 40/0.20 | 0.8 | 9.9 | 101.4 | 1749 |
| 300 | 854/0.67 | 5.0 | 7/0.50 | 71.5 | 40/0.20 | 0.8 | 10.4 | 109.3 | 2120 |
| Type 409.11 Class2 |
| 25 | 209/0.40 | 7.6 | 7/0.25 | 23.7 | 24/0.20 | 0.8 | 8.1 | 75.6 | 750 |
| 35 | 285/0.40 | 7.6 | 7/0.30 | 30.2 | 24/0.20 | 0.8 | 8.4 | 79.7 | 859 |
| 50 | 380/0.40 | 7.6 | 7/0.30 | 31.7 | 40/0.20 | 0.8 | 8.7 | 83.6 | 954 |
| 70 | 203/0.67 | 7.6 | 7/0.30 | 34.1 | 40/0.20 | 0.8 | 9.1 | 88.8 | 1105 |
| 95 | 259/0.67 | 7.6 | 7/0.40 | 47.5 | 40/0.20 | 0.8 | 9.6 | 93.7 | 1290 |
| 120 | 336/0.67 | 7.6 | 7/0.40 | 51.0 | 40/0.20 | 0.8 | 9.9 | 98.8 | 1460 |
| 150 | 427/0.67 | 7.6 | 7/0.40 | 53.7 | 40/0.20 | 0.8 | 10.3 | 103.5 | 1636 |
| 185 | 518/0.67 | 7.6 | 7/0.40 | 57.2 | 40/0.20 | 0.8 | 10.7 | 108.8 | 1830 |
| Type 409.22 Class2 |
| 35 | 285/0.40 | 10.5 | 7/0.40 | 55.4 | 24/0.20 | 0.8 | 10.0 | 105.0 | 1405 |
| 50 | 380/0.40 | 10.5 | 7/0.40 | 58.1 | 40/0.20 | 0.8 | 10.3 | 108.9 | 1525 |
| 70 | 203/0.67 | 10.5 | 7/0.40 | 60.7 | 40/0.20 | 0.8 | 10.7 | 114.0 | 1710 |

www.caledonian-cables.co.uk  www.addison-cables.com	27