Caledonian Mining Cables

Mine Power Feeder Cables

Type MP-GC Three-Conductor

Mine Power Feeder Cable, CPE Jacket, 25kV

� Applications .............................................................................................................

These cables are designed for connections between units of mine distribution systems, suitable for installed in duct, conduit or open air and for direct burial in wet and dry locations�

�  Standards

................................................................................................................

ICEA S-75-381/NEMA WC 58 ASTM B-8

CAN/CSA-C22�2 No�96

� Construction ............................................................................................................

Ground Check Conductor Stranded Bare Copper Conductor Conductor Shield

Grounding Conductor EPR Insulation Insulation Shield CPE Jacket

Conductors:

Stranded annealed bare copper conductor�

Conductor  Shield: Conducting layer� Insulation:

Ethylene Propylene Rubber (EPR)�

Insulation  Shield: Conducting layer + copper tape� Ground  Check  Conductor:

Copper conductor with a yellow polypropylene insulation�

www.caledonian-cables.co.uk  www.addison-cables.com	65

Caledonian Mining Cables

Mine Power Feeder Cables

Grounding  Conductor: Tinned copper conductor� Jacket:

Chlorinated Polyethylene (CPE), black�

� Options .....................................................................................................................

Other jacket materials such as CSP/PCP/NBR/PVC/TPU are available upon request�

�  Mechanical and Thermal Properties ......................................................................

Minimum Bending Radius: 12�OD

Maximum Conductor Operating Temperature: +90℃

�  Dimensions and Weight

........................................................................................

| Construction | No. of Strands | Grounding Conductor Size | Ground Check Conductor Size | Nominal Insulation Thickness | Nominal Jacket Thickness | Nominal Overall Diameter | Nominal Weight | Ampacity |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| No. of cores�AWG/ kcmil | - | AWG/ kcmil | AWG/kcmil | inch | mm | inch | mm | inch | mm | lbs/kft | kg/km | A |
| 3�1 | 19 | 5 | 8 | 0�260 | 6�4 | 0�14 | 3�6 | 2�37 | 60�2 | 3435 | 5112 | 187 |
| 3�1/0 | 19 | 4 | 8 | 0�260 | 6�4 | 0�14 | 3�6 | 2�45 | 62�2 | 3815 | 5677 | 218 |
| 3�2/0 | 19 | 3 | 8 | 0�260 | 6�4 | 0�14 | 3�6 | 2�54 | 64�5 | 4290 | 6384 | 249 |
| 3�3/0 | 19 | 2 | 8 | 0�260 | 6�4 | 0�14 | 3�6 | 2�65 | 67�3 | 4875 | 7255 | 286 |
| 3�4/0 | 19 | 1 | 8 | 0�260 | 6�4 | 0�14 | 3�6 | 2�81 | 71�4 | 5665 | 8430 | 327 |
| 3�250 | 37 | 1/0 | 8 | 0�260 | 6�4 | 0�17 | 4�3 | 2�97 | 75�4 | 6495 | 9666 | 360 |
| 3�350 | 37 | 2/0 | 8 | 0�260 | 6�4 | 0�17 | 4�3 | 3�18 | 80�8 | 7970 | 11860 | 438 |
| 3�500 | 37 | 4/0 | 8 | 0�260 | 6�4 | 0�17 | 4�3 | 3�45 | 87�6 | 10300 | 15328 | 536 |

Ampacity-Based on a conductor temperature of 90℃ and an ambient air temperature of 40℃, per ICEA S-75-381�

66	www.caledonian-cables.co.uk  www.addison-cables.com